## Slide 1
NS-P02 / 01
Firewall & NAT Security Lab
NS-P02 | Manufacturing Company
• Four-zone manufacturing security redesign
• Offline browser model with Cisco configuration build kit
• Validated policy behavior; Cisco topology execution remains unrun
Notes: This demonstration implements a four-zone policy model for a manufacturing scenario. It runs offline in a browser. Cisco configuration files accompany the model, but I do not claim they have been executed in Packet Tracer.

## Slide 2
NS-P02 / 02
Threat model
Why a flat IT/OT network is risky
• Compromised corporate hosts can attempt lateral access to OT
• Telnet exposes credentials in cleartext
• Unrestricted outbound flows can enable exfiltration
• Permitted HTTPS still needs endpoint and application controls
Notes: A flat architecture makes it easier for a corporate compromise to reach critical systems. Segmentation adds checkpoints. Blocking Telnet and unauthorized outbound ports reduces exposure, but allowed HTTPS can still carry harmful traffic.

## Slide 3
NS-P02 / 03
Four security zones
VLANs and routed security boundaries
• Internet: gateway 203.0.113.2; lab web 198.51.100.10
• Corporate VLAN 10: 192.168.10.0/24
• Factory OT VLAN 20: 192.168.20.0/24
• Admin VLAN 30: 192.168.30.0/24; jump host .10
Notes: The gateway separates Corporate, Factory OT, Administration and the simulated Internet. Corporate initiations to OT and Admin are denied. Hosts within a VLAN bypass gateway filtering, so this is not complete host isolation or a physical air gap.

## Slide 4
NS-P02 / 04
Firewall and PAT
Explicit permits, followed by default deny
• Corporate/Admin: TCP 443 and DNS to 8.8.8.8
• Jump host only: internal SSH and SCADA TCP 3389
• OT: no initiated cross-zone traffic and no PAT
• Corporate/Admin share public address through PAT
• Browser replies match tuples; Cisco ACLs are stateless
Notes: Default deny drops routed flows unless a rule permits them. PAT maps allowed outbound flows to one public address with distinct ports. It does not guarantee topology secrecy. Cisco established ACL rules inspect ACK or RST flags rather than tracking sessions.

## Slide 5
NS-P02 / 05
Verification results
Measured checks, with evidence boundaries
• 20 browser checks passed; desktop/mobile controls verified
• 16 Python test methods passed
• 5,334 Corporate boundary cases and 253 admin-source cases checked
• PAT reuse, port uniqueness, allowed replies and denied pivots verified
• No real TLS/SSH/RDP or Packet Tracer traffic was tested
Notes: I can show the browser validation suite, PAT table, decision log, matching replies and rejected wrong-source replies. Automated tests also evaluate the limited syntax used by our Cisco ACLs. These are model and static analysis results, not observed IOS counters or encrypted application handshakes.

## Slide 6
NS-P02 / 06
Limits and recommendations
What remains outside this implementation
• Local read-only SQLite demo verified; network service remains unrun
• Full TCP state, expiration and industrial DPI are not implemented
• Physical USB threats and same-VLAN access remain
• Production: endpoint hardening, industrial NGFW and data diodes
• Packet Tracer is optional for this demo but required for original Cisco validation
Notes: A separate real SQLite demonstration now verifies read-only telemetry queries and rejected writes. A narrow reporting exception is modeled for Corporate host 192.168.10.60 to OT service 192.168.20.10 on TCP 8443. This is an explicit design assumption, not a running network service. Industrial inspection and hardware one-way gateways are future controls. The original Cisco execution requirement remains unfulfilled.